## Slide 1
Course Name: Hardware Security
Faculty Name: Prof Debdeep Mukhopadhyay
Department : Computer Science and Engineering
Topic
Lecture 12: Hardware Implementation of Advanced Encryption

## Slide 2
Concepts Covered:
AES Implementation
Mix Columns Implementation
S-Box Implementation Approaches
Composite Field AES
Intel AES Instruction

## Slide 3: Cryptography Implementations
Important Paradigms
Faster
  Higher Clocks
  Parallelism
  Large Bandwidth
Smaller
  Low Power
  Smaller Area
Both Applications require security

## Slide 4: Design Strategies
2 Strategies to develop efficient hardware
  Algorithmic optimizations:Based on mathematical formulations that take advantage of the hardware platform.
  Architectural optimizations: Exploit architectural techniques such as pipelining, parallelism,

## Slide 6: AES Challenges for the Hardware Designer
Reduce area required
Increase throughput
A unified AES engine for both encryption and decryption
Able to handle different key sizes

## Slide 7: Mix Column Implementation
Multiplying by 2
F.R.Henríquez et. l., Cryptographic Algorithms on Reconfigurable Hardware, Springer series on Signals and Communication Technology, ISBN 0-387-33883-7
a
b
c
d
2x
XOR
2x
XOR
b
XOR
XOR
XOR
2x
2x
c
d
a
c
d
a
b
d
a
b
c
XOR
XOR
XOR
key
Notes: 7

## Slide 8: S-box Implementation in Hardware
Using Tables
  requires 256 byte table
  Slow due to the Von Neumann Bottle neck
  Large area requirements
  Suited for software implementations
Using Logical Equations

## Slide 9: S-box Using Equations
Naïve Method for Sbox(x)
  Compute the inverse of x in GF(28) using the extended Euclidean algorithm
  Apply the affine transformation
Requires several
clock cycles
Using Composite Fields
  Requires just around 100 gates and can be a combinational circuit.

## Slide 10: Composite Fields
Map
Inverse in Composite Field
eg. In GF((24)2)
Reverse
Map
x
Sbox(x)
AES uses the binary finite field GF(28) with irreducible polynomial
The AES field GF(28) is isomorphic to the field GF((24)2) and even GF(((22)2)2)
  This means that we could find the inverse of
  x Є GF(28) by using a smaller field (eg. GF(24))
    Thus smaller tables or equations required
Affine Transform
Notes: 10

## Slide 11: Mapping the Composite Field
Map the field GF(28) to the field GF((22)2)2)
C.Paar, Efficient VLSI Architectures for Bit Parallel Computation in Galois Fields, PHD Thesis, 1998

## Slide 12: S-box Based on Composite Fields
S-box Approach
S-box Approach | No. of Slices | Critical Path | Gate Count
Lookup table based | 64 | 11.9ns | 1128
Composite Field based | 30 | 18.3ns | 312
Performance of S-boxes on FPGA*
XOR | NAND | NOR | Total Gates in terms of NAND (using std cell lib)
80 | 34 | 6 | 180
Gate Count for composite Sbox#
# D. Canright, A Very Compact S-box for AES, CHES-2005
* Simulation Results using Xilinx ISE

## Slide 13: Inverse S-box
Type | XOR | NAND | NOR | NOT | MUX | Total Gates in terms of NAND gates using std cell library
InvS-box | 81 | 34 | 6 | 0 | 0 | 182
Gate Count #
# D. Canright, A Very Compact S-box for AES, CHES-2005

## Slide 14: Overhead of Composite Field s-boxes
Composite field s-boxes require mapping and reverse mapping to and from the composite fields in each round
An alternate approach is to convert all other round operations into composite field operations.
  This would require just one mapping and one reverse mapping for the entire encryption
  Operations Add Round Key and Shift Rows are not altered.
  Mix Columns will need to be re-implemented

## Slide 15: High Speed AES Encryption-Decryption Architecture
Key-Gen
Key
Memory
Encrypt
Decrypt
Mux
Dispatch
Unit
Data
Schedule
Divide
by 4 clock
Ciphertext
Input Data
clock
Enc/ Dec
Multiplexing
Pipelining
Instantaneous toggle between
Encrypt and decrypt
Galois Subfield
D. Mukhopadhyay et. al, An Efficient End to End Design of Rijndael Cryptosystem in 0.18μ CMOS, VLSID 2005

## Slide 16: SubBytes in Composite Fields
In composite fields, where the affine matrixes A and B are updated as:

## Slide 17: Effect on the matrix values of the Affine Transformation
The irreducible polynomial used is say . Here is a primitive element of . We choose, where is an element in .
A key point is that depending on the choice above the matrix A’ will change, and also its cost.
For example, with the above choice let us compare with the original matrix for AES. The number of 1s reduce from 40 to 18!!!

## Slide 18: Mix Columns in Composite Fields
In Composite Fields
Consider the composite field GF((24)2) with
irreducible polynomial
Every element in this field is represented
as a1x + a0 , where a1 and a0 Є GF(24)

## Slide 19: The Decryption Flow
Add Round Key
Buffer
Byte Sub
Shift Row
Mix Column
Buffer
Add Round Key
Buffer
Byte Sub
Shift Row
Add Round Key
Buffer
Keymem
Keymem
Keymen
Add Round Key
Buffer
InvShift Row
Inv Byte Sub
Add RoundKey
Buffer
Inv Mix Column
Buffer
Inv Shift Row
Inv Byte Sub
Add Round Key
Buffer
Keymem
Keymem
Keymem
Add Round Key
Buffer
Inv ByteSub
Inv Shift Row
Inv Mix Column
Buffer
Add Round Key
Buffer
Inv Byte Sub
Inv Shift Row
Add Round Key
Buffer
Keymem
Keymem
Inv Mix
Column

## Slide 20: Compact Encryption-Decryption Architecture
Merge the operations in the encryption and decryption into a single unit.
Key-Gen
Key
Memory
Encrypt/
Decrypt
Dispatch
Unit
Data
Schedule
Input Data
Enc/ Dec

## Slide 21: Merged Round Operations
Addroundkey is the same in both encryption and decryption
ShiftRows and InverseShiftRows only differ in the direction of shifting

## Slide 22: Merged Mix Columns
 | Separate Mix (Inv) Columns | Merged Mix Columns
No. of XOR gates | 152 + 440 = 592 | 195
Delay (gates) | 5 | 7
A. Satoh et. al., A compact Rijndael Hardware Architecture with S-box Optimization, ASIACRYPT 2001

## Slide 23: Merged S-boxes
Map
Inverse in Composite Field
eg. In GF((24)2)
Reverse
Map,
Affine
x
or
Sbox[x]
Sbox[x]
or x
Map,
Revse Affine
Reverse
Map
Type | Total Gates in terms of NAND gates using std cell library
Sbox + InvSbox | 362
Merged | 234
# D. Canright, A Very Compact S-box for AES, CHES-2005

## Slide 24: Different Schools of Designs
Alam
Verbauwhede
Wolkerstorfer
Hodjat
Satoh
J.Wolkerstorfer, E.Oswald and M. Lamberger: An ASIC Implementation of the AES S-boxes: in Proc. RSA Conference (CT-RSA) 2002, LNCS Vol. 2271, pp.67-78, San Jose, CA, Feb. 2002.
M. Alam et. al., An Area Optimized Reconfigurable Encryptor for AES-Rijndael, DATE 2007
A. Satoh et. al., A compact Rijndael Hardware Architecture with S-box Optimization, ASIACRYPT 2001
I. Verbauwhede, P. Schaumont, H. KuoDesign and Performance Testing of a 2.29-GB/s Rijndael Processor, IEEE Journal of Solid State Circuit, 2003.
A . Hodjat et. al. Area Throughput Tradeoffs for Fully Pipelined 30 to 70 Gbits/s AES Processors, IEEE Trans on Computers 2006

## Slide 25: State of the Art
Intel has introduced dedicated hardware for AES on its microprocessors
These are accessed by dedicated AES instructions
The AES design consists of:
  Standard techniques used such as composite fields, single map – reverse map, etc.
  Speed of 53Gbps obtained by fully custom design flow on 45nm technology.
S. Mathew, 53Gbps Native GF(24)2 Composite Field AES-Encrypt/Decrypt Accelerator for Content Protection in 45nm
High Performance Microprocessors,VTS 2010

## Slide 26: Intel’s AES Hardware
S. Mathew, 53Gbps Native GF(24)2 Composite Field AES-Encrypt/Decrypt Accelerator for Content Protection in 45nm
High Performance Microprocessors,VTS 2010

## Slide 28
Conclusion:
Design of AES
Design of Sub-block of AES:
Mix Columns
S-Box
Design of S-Box is challenging
Techniques using Isomorphism seem promising to realize compact S-Boxes.