## Slide 1
Course Name: Hardware Security
Faculty Name: Prof Debdeep Mukhopadhyay
Department : Computer Science and Engineering
Topic
Lecture 14: Hardware Implementation of Advanced Encryption (contd.)

## Slide 2
Concepts Covered:
AES in Composite Fields
Mix Columns Implementation
S-Box Implementation Approaches
Composite Field AES
Intel AES Instruction

## Slide 3: SubBytes in Composite Fields
In composite fields, where the affine matrixes A and B are updated as:
It may be emphasized that due to the isomorphism property,
Thus, we apply the transformed matrices A’ and B’ on the data which is in the composite field. Thus we can avoid the intermediate field transformations.

## Slide 4: Effect on the matrix values of the Affine Transformation
The irreducible polynomial used is say . Here is a primitive element of . We choose, where is an element in .
A key point is that depending on the choice above the matrix A’ will change, and also its cost.
For example, with the above choice let us compare with the original matrix for AES. The number of 1s reduce from 40 to 18!!!

## Slide 5: Transforming GF(28) to GF(24)2
Previous efficient technique works when all field polynomials are primitive.
However, in case of AES the field polynomial is irreducible but not primitive.
Since the field is small our exhaustive technique can be applied.
Basic idea was mapping a primitive element of , say to a primitive element of , say .
For the remaining elements we map

## Slide 6: An Example T from GF(28) to GF(24)2
Consider ie can be denoted as (0000 0010).
Thus, T(2) would be in GF(24)2, ie. (0010 1110)=where is the primitive element of GF(24), modulo .
Atri Rudra, Pradeep K. Dubey, Charanjit S. Jutla, Vijay Kumar, Josyula R. Rao, Pankaj Rohatgi:Efficient Rijndael Encryption Implementation with Composite Field Arithmetic. CHES 2001: 171-184

## Slide 7: Mix Columns in Composite Fields
In Composite Fields
Consider the composite field GF((24)2) with
irreducible polynomial
Every element in this field is represented
as a1x + a0 , where a1 and a0 Є GF(24)

## Slide 8: The Decryption Flow
Add Round Key
Buffer
Byte Sub
Shift Row
Mix Column
Buffer
Add Round Key
Buffer
Byte Sub
Shift Row
Add Round Key
Buffer
Keymem
Keymem
Keymen
Add Round Key
Buffer
InvShift Row
Inv Byte Sub
Add RoundKey
Buffer
Inv Mix Column
Buffer
Inv Shift Row
Inv Byte Sub
Add Round Key
Buffer
Keymem
Keymem
Keymem
Add Round Key
Buffer
Inv ByteSub
Inv Shift Row
Inv Mix Column
Buffer
Add Round Key
Buffer
Inv Byte Sub
Inv Shift Row
Add Round Key
Buffer
Keymem
Keymem
Inv Mix
Column

## Slide 9: Some Points
The order of InvShift Rows and InvSubBytes is indifferent.
The order of AddRoundKey and InvMixColumns can be inverted if the round key is adapted accordingly.

## Slide 10: A Linear transformation can be pushed through an XOR
L
k
x
L
k
x
L

## Slide 11: Encryption steps for two round AES variant
AddRoundKey(State, ExpandedKey[0]);
SubBytes(State);
ShiftRow(State);
MixColumn(State);
AddRoundKey(State, ExpandedKey[1]);
SubBytes(State);
ShiftRow(State);
AddRoundKey(State, ExpandedKey[2]);

## Slide 12: Decryption steps for two round AES variant
AddRoundKey(State, ExpandedKey[2]);
InvShiftRow(State);
InvSubBytes(State);
AddRoundKey(State, ExpandedKey[1]);
InvMixColumn(State);
InvShiftRow(State);
InvSubBytes(State);
AddRoundKey(State, ExpandedKey[0]);

## Slide 13: Equivalent Decryption steps for two round AES variant
AddRoundKey(State, ExpandedKey[2]);
InvSubBytes(State);
InvShiftRow(State);
InvMixColumn(State);
AddRoundKey(State, EqExpandedKey[1]);
InvSubBytes(State);
InvShiftRow(State);
AddRoundKey(State, ExpandedKey[0]);

## Slide 14: Equivalent Decryption
The equivalent key-scheduling can be obtained by applying InvMixColumns after the key-scheduling algorithm.
This can be generalized to the full round AES.
Thus we see that in the equivalent decryption the sequence of steps is similar.
  This helps implementation

## Slide 15: Compact Encryption-Decryption Architecture
Merge the operations in the encryption and decryption into a single unit.
Key-Gen
Key
Memory
Encrypt/
Decrypt
Dispatch
Unit
Data
Schedule
Input Data
Enc/ Dec

## Slide 16: Merged Round Operations
Addroundkey is the same in both encryption and decryption
ShiftRows and InverseShiftRows only differ in the direction of shifting

## Slide 17: Merged Mix Columns
 | Separate Mix (Inv) Columns | Merged Mix Columns
No. of XOR gates | 152 + 440 = 592 | 195
Delay (gates) | 5 | 7
A. Satoh et. al., A compact Rijndael Hardware Architecture with S-box Optimization, ASIACRYPT 2001

## Slide 18: Another InvMixColumn Design
Gate-count around 166 XORs and a 32-bit MUX.
Subhadeep Banik, Andrey Bogdanov, Francesco Regazzoni:Atomic-AES: A Compact Implementation of the AES Encryption/Decryption Core. INDOCRYPT 2016: 173-190

## Slide 19: Merged S-boxes
Map
Inverse in Composite Field
eg. In GF((24)2)
Reverse
Map,
Affine
x
or
Sbox[x]
Sbox[x]
or x
Map,
Revse Affine
Reverse
Map
Type | Total Gates in terms of NAND gates using std cell library
Sbox + InvSbox | 362
Merged | 234
# D. Canright, A Very Compact S-box for AES, CHES-2005

## Slide 20: Different Schools of Designs
Alam
Verbauwhede
Wolkerstorfer
Hodjat
Satoh
J.Wolkerstorfer, E.Oswald and M. Lamberger: An ASIC Implementation of the AES S-boxes: in Proc. RSA Conference (CT-RSA) 2002, LNCS Vol. 2271, pp.67-78, San Jose, CA, Feb. 2002.
M. Alam et. al., An Area Optimized Reconfigurable Encryptor for AES-Rijndael, DATE 2007
A. Satoh et. al., A compact Rijndael Hardware Architecture with S-box Optimization, ASIACRYPT 2001
I. Verbauwhede, P. Schaumont, H. KuoDesign and Performance Testing of a 2.29-GB/s Rijndael Processor, IEEE Journal of Solid State Circuit, 2003.
A . Hodjat et. al. Area Throughput Tradeoffs for Fully Pipelined 30 to 70 Gbits/s AES Processors, IEEE Trans on Computers 2006

## Slide 21: State of the Art
Intel has introduced dedicated hardware for AES on its microprocessors
These are accessed by dedicated AES instructions
The AES design consists of:
  Standard techniques used such as composite fields, single map – reverse map, etc.
  Speed of 53Gbps obtained by fully custom design flow on 45nm technology.
S. Mathew, 53Gbps Native GF(24)2 Composite Field AES-Encrypt/Decrypt Accelerator for Content Protection in 45nm
High Performance Microprocessors,VTS 2010

## Slide 22: Intel’s AES Hardware
S. Mathew, 53Gbps Native GF(24)2 Composite Field AES-Encrypt/Decrypt Accelerator for Content Protection in 45nm
High Performance Microprocessors,VTS 2010

## Slide 24
Conclusion:
Expressing AES in composite fields.
Techniques using Isomorphism efficient for S-boxes.
MixColumns and Inverse MixColumns can be efficiently combined.
Encryption and decryption of AES can be made similar by using its structure.
Combined encryption and decryption saves gates.