## Slide 1
Course Name: Hardware Security
Faculty Name: Prof Debdeep Mukhopadhyay
Department : Computer Science and Engineering
Topic
Lecture 05: Finite Field Architectures-2

## Slide 2
Concepts Covered:
Karatsuba Multipliers
Modulo Operation in GF(2)

## Slide 3: Example
233 bit Hybrid Karatsuba Multiplier

## Slide 4: Module Multiplier in Verilog
module multiplier(a, b, d);
input wire [232:0] a;
input wire [232:0] b;
output wire [232:0] d;
wire [464:0] mout;
ks233 ks(a, b, mout); (Karatsuba Multiplier)
mod mod1(mout, d); (Modulo Operation)
endmodule

## Slide 5: Karatsuba Multiplier
The multiplier operates on 233 bit inputs and gives a 465 bit outputs.
The multiplier uses sub-multipliers, with operands as described in the figure.
The initial multipliers are Simple Karatsuba based, however after a threshold of 16, it was realized by Generalized Karatsuba blocks.

## Slide 6: Module ks233
module ks233(a, b, d);
input wire [232:0] a; input wire [232:0] b;
output wire [464:0] d;
wire [230:0] m1; wire [232:0] m2;
wire [232:0] m3;wire [116:0] ahl; wire [116:0] bhl;
ks117 ksm1(a[116:0], b[116:0], m2);
ks116 ksm2(a[232:117], b[232:117], m1);
assign ahl[115:0] = a[232:117] ^ a[115:0];
assign ahl[116] = a[116];
assign bhl[115:0] = b[232:117] ^ b[115:0];
assign bhl[116] = b[116];
ks117 ksm3(ahl, bhl, m3);
endmodule

## Slide 7: Combining the Partial Results
Since, n=233:
  d[0…116] = m2[0…116]
  d[117…232]=m2[117…232] ^ m2[0..115] ^ m1[0…115] ^ m3[0…115]
  d[233]=m2[116]^m1[116]^m3[116]
  d[234…347]=m2[117…230]^m1[117…230]^m3[117…230]^m1[0…113]
  d[348] = m2[231] ^ m3[231] ^ m1[114]
  d[349] = m2[232] ^ m3[232] ^ m1[115]
  d[350…464]=m1[116…232]

## Slide 8: Generalized Karatsuba
A(x)=a2x2+a1x+a0, B(x)=b2x2+b1x+b0
D0=a0b0, D1=a1b1, D2=a2b2
D0,1=(a0+a1)(b0+b1), D0,2=(a0+a2)(b0+b2)
D1,2=(a1+a2)(b1+b2)
A(x)*B(x)
=D2x4+(D1,2-D1-D2)x3+(D0,2-D0-D2+D1)x2+(D0,1-D0-D1)x+D0

## Slide 9: The Generalized Karatsuba Codes
module ks14(a, b, d) and module ks15(a, b, d)
uses this idea for 14 and 15 degree polynomials.
Details can be found in the verilog code:
http://cse.iitkgp.ac.in/~debdeep/osscrypto/eccpweb/downloads/ksgen_verilog.tar.gz

## Slide 10: Modulo Operation
Multiplication and squarer will lead to overflow.
  Hence we need to perform a modulo operation to bring the result in the field
Modulo Polynomial:
x233+x74+1
Here, m=233 and n=74
(Note: n < m/2)

## Slide 12
Conclusion:
We studied few important finite field operations in characteristic 2:
Karatsuba Multipliers
Squaring
Modulo Operation