## Slide 1
Course Name: Hardware Security
Faculty Name: Prof Debdeep Mukhopadhyay
Department : Computer Science and Engineering
Topic
Lecture 7: Hardware Design for Finite Field Inverse

## Slide 2
Concepts Covered:
Hardware Design of Itoh-Tsujii
Performance of the Hardware Circuit

## Slide 3: Quad Itoh Tsujii Algorithm
We now require 115 quads (instead of 232) and 9 multiplications. We save 7 clock cycles.
We set n=2
Initial Pre-computation:
To compute the cube, the multiplier is used for 2 clock cycles. Remember there is no squarer.
Likewise, the final squaring also is done by a multiplication step.
So, in total 12 multiplications.

## Slide 4: Estimating the number of clock cycles
#Multiplications: l-2+3=l+1. Note that 2 multiplications are needed initially for pre-computation, and one for final squaring.
Difference in clock cycle:
This can be as high as (m-1)/2 for GF(2m)

## Slide 5: Hardware Architecture for Quad ITA

## Slide 6: Control Word Design

## Slide 7: Number of Cascades
Number of quad circuits (us) has an influence on the clock-cycles, frequency, and area requirements.
Decreasing us would reduce area, but also increase clock cycles.
Let a quad circuit require lp LUTs and have a combinational delay of tp.
A cascade of us quad circuits would require us. lp LUTs and have a delay of us. tp .
In order that the quadblock does not alter the frequency of operation us should be selected such that us. tp is less than the critical path, which is of the multiplier circuit.
So, we make us. tp close to the multiplier delay.

## Slide 8: Number of Cascades
Experiments on Virtex-4 FPGA for GF(2233)

## Slide 9: Performance of Quad-ItohTsujii on Virtex 4 and 5 Platforms
Virtex 4
Virtex 5
Quad ITA
Squarer ITA
C. Rebeiro et. al. Revisiting the Itoh-Tsujii Inversion Algorithm for FPGA Platforms, IEEE TVLSI
Performance=Frequency/(Slices x ClockCycles)

## Slide 10: Performance of Inversion Hardware on Xilinx Virtex E

## Slide 12
Conclusion:
We studied a very important finite field operations in characteristic 2:
Finite Field Inverse
Itoh-Tsujii Inversion Algorithm
Generalization
Hardware Design of finite Field Inverse